## Slide 1: Riparian Evaluation System (RipES): Remedial Design Tool for the Cleanup of the Clark Fork River
Authors:
Dr. Paul L. Hansen Dennis R. Neuman
William H. Thompson Stuart R. Jennings

## Slide 2: History of RipES
Initial RipES document (RRU and RWRP 2000).
Feasibility Study completed.
Proposed Plan for Clark Fork River Operable Unit (CFR OU).
Possible to make modification to the system compatible with conceptual thinking and rationale found in the Proposed Plan.
Field work completed in fall 2002.
Updated RipES document in January 2003.
Field validation in summer of 2003.
Record of Decision in April 2004.

## Slide 3: Initial Development of RipES and Field Testing
Combination of the Riparian and Wetland Health Assessment Protocols and the Land Reclamation Evaluation System (LRES).
Riparian and Wetland Health Assessment Protocols are used to assess the health of streams, rivers, potholes, lakes, and reservoirs throughout the western United States and Canada. Initial development started in 1987.
LRES was designed to assess the effects of mining and smelting contamination on predominantly upland areas.

## Slide 4: Initial Development of RipES and Field Testing
What ecological parameters to evaluate?
How to assign a scoring system?
Weight scores for the identified parameters.
Eliminate repetition.
Repeatability.
Limit ambiguity or variability.
Field testing in 2000, 2001, and 2002.
Field validation in 2003.

## Slide 5: CFR-RipES Validation
Iterative process of adjusting scores among evaluation attributes.
Score impacted and slightly impacted soils and vegetation polygons to set limits.
Refine scoring.
Neuman

## Slide 6: Data Quality Objectives
Data Quality Objectives provide a systematic planning tool based on the scientific method (APHA 1998). This process documents the criteria for defensible decision-making before an environmental data collection activity begins.
EPA Process
Problem statement.
Identify decisions and actions.
Identify inputs.
Identify spatial and temporal limits.
Develop a decision rule.
Specify limits on decision errors.
Optimize design for collection.

## Slide 7: DQO Decisions for CFR-RipES
What information and data are required to categorize streambanks as Class 1, 2, or 3 (identified/described in the Feasibility Study and the Proposed Plan)?
What characteristics (chemical, physical, and biological) define slickens, impacted soils and vegetation areas, or unimpacted areas?
How should streambank stability and contamination severity be evaluated for streambank polygons?
How should ecological dysfunction and contamination severity be evaluated for impacted soils and vegetation polygons?
What data and information are required to support selection of a preliminary remedial action for a specific polygon?
Several other questions are posed in the CFR-RipES document.

## Slide 8: CFR RipES Structure
Four major types of sites for the purpose of identifying areas for the various remedial actions:
Streambank and riparian corridor buffer;
Slicken areas (exposed tailings);
Impacted soils and vegetation areas; and
Slightly impacted soils and vegetation areas.

## Slide 9: CFR RipES Definitions
Slickens (exposed tailings)—areas that generally lack vegetation and present a principal waste in the Clark Fork River Operable Unit, along with Class 1 Streambanks.
Slickens are characterized as follows:
Because of phytotoxic conditions, these areas are generally devoid of vegetation, supporting less than 25 percent live plant canopy cover.
Tufted hairgrass (Deschampsia cespitosa) is present, if there is any live vegetation.
Efflorescent metal salts are visible on the soil surface during dry periods.
Slickens and underlying contaminated soil which meet these criteria will be removed, with limited exception.

## Slide 10: CFR RipES Definitions
Impacted soils and vegetation areas—these sparsely vegetated areas amount to everything between slickens and slightly impacted soils and vegetation areas. Impacted soils and vegetation areas will generally be treated in-situ, unless the tailings and impacted soils in a given area extend more than 2 feet below ground surface. In that case, the tailings and impacted soils will be removed.

## Slide 11: CFR RipES Definitions
Impacted soils and vegetation areas are characterized by the following:
The degree of phytotoxicity in these areas is quite variable, but they do sustain at least 25 percent live plant canopy cover.
Tufted hairgrass (Deschampsia cespitosa) has greater than 1 percent canopy cover.
Efflorescent metal salts may be visible on the soil surface during dry periods.
Small, individual areas of exposed tailings (that appear as small slickens) may be present.
Concentrations of COCs within the soil profile exceed the geometric mean values for unimpacted soils for Reach A of the CFR OU. Copper is used as a surrogate for the COCs; soils with copper concentrations exceeding 300 ppm within the profile are considered impacted by mining-related activities.
The minimum polygon size is 400 square feet.

## Slide 12: CFR RipES Definitions
Slightly impacted soils and vegetation areas—these areas do not meet the characteristics or definitions of streambank and riparian corridor buffers, slickens (exposed tailings), or impacted soils and vegetation area. They are generally well vegetated and display no visible evidence of contamination from tailings, although the soil may contain copper contamination above 300 ppm. Remedial actions for these areas are no action, or BMPs and ICs.

## Slide 13: CFR RipES Definitions
Slightly impacted soils and vegetation areas are characterized by the following:
The area expresses no evidence of phytotoxicity and has less than 1 percent bare ground caused by contaminated tailings.
Tufted hairgrass (Deschampsia cespitosa) has less than 1 percent canopy cover.
No efflorescent metal salts are visible on the soil surface during dry periods.
Concentrations of COCs within the soil profile exceed the geometric mean values for unimpacted soils for Reach A of the CFR OU. Copper is used as a surrogate for the COCs; soils with copper concentrations exceeding 300 ppm within the profile are considered impacted by mining-related activities.

## Slide 14: CFR-RipES Process
The RipES process can be applied in a series of steps beginning with delineating areas having similar ecological attributes on aerial photographs and ending by generation of sufficient data and information to allow for final remedial design.
Use of RipES in post-RD/RA activities.

## Slide 15: Post-RD/RA RipES Use
Setting performance standards for remediated areas:
Vegetation component;
Landscape stability; and
Land use.
Success Evaluation:
Operational and Functional Determination of Remedy;
Monitoring and Maintenance; and
Delisting.

## Slide 16: CFR-RipES Summary
Is a Remedial Design Tool.
Uses Data Quality Objectives for defensible decision making in design.
Links mining related pollution to remedial action.
Considers lands within the historic 100 year floodplain.
May be applied to post RD/RA applications for success evaluations, O&F determinations, and monitoring and maintenance.

## Slide 17
Clark Fork River Class 1 Streambank adjacent to a slickens area (exposed tailings)

## Slide 18
Highly eroding Clark Fork River Class 2 Streambank

## Slide 19
Clark Fork River Class 3 Streambank with visible tailings and
appropriate deep, binding, woody vegetation

## Slide 20
Clark Fork River slickens area (exposed tailings)

## Slide 21
Clark Fork River slickens (exposed tailings) surrounded by pioneer species such as
tufted hairgrass (Deschampsia cespitosa) and redtop (Agrostis stolonifera)

## Slide 22
Clark Fork River slickens (exposed tailings) showing extensive areas of metal salts
along with less than 25 percent vegetative canopy cover

## Slide 23
Clark Fork River slickens area (exposed tailings) showing some metal salts, less than 25 percent
vegetative canopy cover, and tufted hairgrass (Deschampsia cespitosa) along the perimeter

## Slide 24
Example of a Clark Fork River impacted soils and vegetation area

## Slide 25
Example of a Clark Fork River impacted soils and vegetation area in foreground
surrounded by a stand of water birch (Betula occidentalis) and willows

## Slide 26
Example of a Clark Fork River slightly impacted soils and
vegetation area used as a cattle pasture

## Slide 27
Hay meadow containing a Clark Fork River slightly impacted soils and vegetation area