## Slide 1
Effects of mine remediation over large spatial and temporal scales
Michelle Hornberger1
Samuel Luoma1
Michael Johnson2
Marcel Holyoak2
1U. S. Geological Survey
2UC Davis
Notes: Primary purpose of this talk is to evaluate copper trends in the Clark Fork River with respect to both natural and anthropogenic events that have occurred over the course of our study.
As remediation efforts are underway, there is a need to identify environmental responses to those efforts, especially when those efforts have occurred under variable environmental conditions (e.g., different flow regimes).

## Slide 2
Long term monitoring commitment
Associate observed trends to causal mechanisms.
Identify proper spatial and temporal scale
Consistency between chosen response variable and scale.
Measure of ecosystem response
Environmental indicators of physical, chemical and/or biological conditions.
Criteria for environmental trend detection
Notes: Important to identify certain parameters in order to detect trends:
First, identify what type of environmental measure will be used to determine ecosystem response (environmental measure, e.g., water, sediment, bioassessment…). Recognize the strengths and limitations of the environmental indicator.
Deal with the issue of scale: inconsistent scaling factors can increase variability. Need systematic sampling design over both time and space in order to detect trends. (could be easy to miss important events w/ inconsistent sampling). Inconsistent sampling can also reduce statistical power to quantify trend data. For example: for spatial scale, you wouldn’t use just one station to characterize the entire river. In terms of temporal scale, high seasonal variability would make one annual sample for water quality meaningless.
In an effort to assign causal associations to observed trends, a long term monitoring commitment is needed to link patterns observed in the field to possible environmental variables (either natural or anthropogenic). Best to have observations over a large range of environmental conditions to strengthen the causal link and to improve predictability as remediation moves forward.

## Slide 3
Measures of ecosystem response…
Floodplains
Stream banks
Tailing Deposits
Sources:
Photo: John Lambing
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
Water
Sediment
Environmental indicators:
Photo: Ed Moon
Biota
Photo: Ed Moon
Bioaccumulation studies integrate metal exposure variables…
Biological sink:
Photo: Ed Moon
USGS, Helena

## Slide 4
Since 1986, sieved bed sediment and aquatic insects have been collected during low flow conditions, typically in August.
Biomonitors
Stonefly
Caddisfly
Samples are processed in the lab and analyzed for a suite of metals (e.g., As, Cd, Cu, Pb, Zn)
Monitoring
Photo: Ed Moon
Photos: Steve Fend
Notes: Since 1986, annual field collections of sieved bed sediment and various species of aquatic insects. Collected during low flow conditions each year.
The study satisfies the spatial component of trend detecting criteria in that it is spatially extensive, extending down from the headwaters below the ponds to below Missoula (Large contamination gradient).
The study also satisfies the temporal component of the criteria because it was designed to be temporally consistent with our environmental measure (coincides with the life-cycle of the biomonitor, Hydropsyche), a univotine species that occurs throughout both the mainstem of the CFR and nearby tributaries.
As such, we feel that the design meets the goals of being temporally and spatially sensitive in detecting trends.

## Slide 5
Remediation can be considered as an anthropogenic variable in the CFR…
Source: CFR-OU, Draft Feasibility Report, 2002
1990
1992
1994
1996
1998
2000
2002
2004
STARS demonstration project
Resource Indemnity Trust CFR demonstration
Streambank stabilization pilot project
Berms installed in the upper 45 Km
Mill-Willow Bypass removal of tailings
Warm Springs Ponds remediation.
Mill-Willow Bypass reconstruction
Insitu treatment of tailings at Deer Lodge
Old Works remediation along WS Creek
Station Km
Notes: Two major variables in the CFR that can influence our field observations. The first is remediation, a large scale manipulation of the landscape, designed to remove the worst of the contamination.
Here’s a general timeline of remediation events since 1989. Dark bars represent major projects. Dash bars represent pilot or demonstration projects. Most of these measures are preliminary as large scale efforts will proceed in the near futures.
To date, all remediation efforts have been isolated upstream of 45 Km (reach A). When full scale remediation begins, those measures will be extended down to Reach B.

## Slide 6
1990
1992
1994
1996
1998
2000
2002
2004
0
100
200
300
400
Total Annual Discharge (cfs x 1000)
Hydrological processes can be considered a natural variable in the CFR…
Goldcreek
Notes: Second major variable to consider when evaluating trends is the hydrologic condition of the river. So, superimposed on the human induced changes to the landscape, there are natural processes that are highly dynamic.
This graph shows an example of a hydrograph since remediation began. Notice that the highest flows occurred in the mid-1990’s and some of the lowest flows have occurred during the last four-five years (drought situation).
Can’t consider that an environmental measure will respond in isolation to remediation. Environmental variability can play an important role.

## Slide 7
2. Spatial variability is an important factor in Reach A.
3. Hydrology influences metal trends in Reaches B and C.
1. Environmental indicators do show a response to remediation.
Points to address…
Station Km
Notes: Rather than start with questions, list the things we already know (and will show in this talk).
Environmental variables do show a response to remediation.
Stations within Reach A are still variable (small scale spatial variability)
Hydrologic processes are important in Reaches B and C.

## Slide 8
Cu concentrations in the upper 7 Km show a temporal response which coincides with remediation …
Biota
Sediment
Pond Outfall
500
1000
1500
1000
2000
3000
1986
1989
1992
1995
1998
2001
2004
0
1986
1989
1992
1995
1998
2001
2004
0
1986
1989
1992
1995
1998
2001
2004
0
20
40
60
80
100
1986
1989
1992
1995
1998
2001
2004
0
50
100
150
200
Copper µg/g
Galen
Regional Background
2. Spatial variability is an important factor in Reach A.
3. Hydrology influences metal trends in Reaches B and C.
1. Environmental indicators do show a response to remediation.
r2=0.47
r2=0.33
r2=0.13
r2=0.24
Notes: To address the first question, we’ll look at two monitoring stations in the upstream reach (a site directly below the ponds, Galen Gage and Deer Lodge). Both indicators show a unidirectional decrease in Cu concentrations that coincide with the general timing of remediation activities. This trend is strongest at the two upstream stations (PO and GG).
Notice that bed sediment concentrations at the two upstream stations (PO and GG) have not only decreased over time, but the temporal variability has also been reduced (very small error bars relative to earlier years).

## Slide 9
However other elements have increased over the same time period...
1992
1994
1996
1998
2000
2002
2004
Arsenic in Biota: Pond Outfall
0
5
10
15
20
30
35
25
Arsenic µg/g
Notes: Not all metals respond similarly over time.
While Cu (and Cd for that matter) have decreased at the two upstream stations, arsenic has increased at the most upstream site (PO). This may be due to the fact that the chemistry of the two elements is different (Cu is a cation and is the target metal for remediation while As is an anion). While we don’t yet know what may be causing these high concentrations, we do know that for three years, As concentrations far exceed long-term As baseline for Hydropsyche at this station.
This is an example where the long-term data set is useful in that we can identify significant temporal changes within a site. If we had only occasionally sampled at this site, the high values from the last three years might have been interpreted as ‘noise’ or outliers. Systematic annual sampling allows us to use historical patterns (in this case, a relatively low long-term average) as a way to understand significant changes that may occur over time.

## Slide 10
Not all stations in ‘Reach A’ show a temporal response coinciding with remediation...
0
500
1000
1500
2000
1990
1992
1994
1996
1998
2000
2002
2004
0
60
120
180
Copper, µg/g
Sediment
Biota
Copper, µg/g
Racetrack: 18 Km
Deer Lodge: 45 Km
2. Spatial variability is an important factor in Reach A.
3. Hydrology influences metal trends in Reaches B and C.
1. Environmental indicators do show a response to remediation.
Notes: We’ve seen that both indicators appear to have responded to remediation in some of the upstream stations. Because remediation has focused specifically on the upper 45 Km, we’d like to know if all stations in this reach respond in a similar temporal pattern. That is, what is the degree of spatial variability within the remediated reach?
If we look at two additional stations within Reach A, we can see that both indicators (sediment plotted on the top graph, Hydropsyche on the bottom) show a high degree of temporal variability. This may indicate isolated ‘hot spots’, areas where localized source inputs override influences of upstream remediation events (at least so far). This also suggests that we shouldn’t expect the river to show a similar temporal response at all stations (again, isolated pockets of highly variable conditions).
Temporal trends related to remediation appears strongest in the most upstream reach, sites where the most extensive remediation has taken place to date.

## Slide 11
Fate and transport of metal in the Reaches B and C are related to hydrologic conditions…
Cu
Cu
Cu
Cu
Cu
Cu
Cu
Cu
Notes: Here’s a conceptual model of how discharge would mobilize metals into the CFR:
During high flow events, increase runoff across contaminated floodplains and slicken deposits; increase scouring and slumping of streambanks, possible increase of ground water.

## Slide 12
Long term monitoring has revealed that stream discharge is an important factor in the distribution and bioavailability of Cu in Reaches B and C.
0
60
120
180
0
100
200
300
400
500
0
400
800
1200
Above Bearmouth: r2=0.72
Goldcreek: r2=0.50
Goldcreek: r2=0.50
Above Bearmouth: r2=0.62
Total annual discharge, cfs (x1000)
Biota
Sediment
Copper, µg/g
Copper, µg/g
Photo: Ed Moon
2. Spatial variability is an important factor in Reach A.
3. Hydrology influences metal trends in Reaches B and C.
1. Environmental indicators do show a response to remediation.
Notes: In the middle and lower reaches (Reaches B and C), concentrations in both indicators increase with increasing flow. In other words, water does not act as a diluent in this system, but acts as a source.
We’ve shown in earlier studies that metal concentrations in the lower reaches (B and C) are highly influenced by discharge. Here we see both indicators responding to temporal variations in hydrology, suggesting that streamflow is an important component in controlling temporal metal concentrations at these reach specific stations (this relationship is not evident upstream in Reach A).

## Slide 13
The temporal pattern of Cu in Reaches B and C correspond to total annual discharge…
Biota
0
60
120
180
0
100
200
300
400
0
50
100
150
0
100
200
300
400
500
0
40
80
120
1986
1989
1992
1995
1998
2001
2004
0
100
200
300
400
500
600
700
800
900
Goldcreek
Above Bearmouth
Turah
Sediment
0
500
1000
1500
0
100
200
300
400
0
300
600
900
0
100
200
300
400
500
1986
1989
1992
1995
1998
2001
2004
0
200
400
600
800
0
100
200
300
400
500
600
700
800
900
Copper, µg/g
Total annual discharge
r2=0.36
r2=0.37
r2=0.23
Notes: Now that we’ve shown that flow is an important factor in controlling the temporal trends of metals in Reaches B and C, we can evaluate the patterns with respect to remediation.
First looking at the graphs on the left, we see that in general, Cu concentrations in bed sediment do decrease over time at the three downstream stations (85 km to 190 km). Although this is a statistically significant relationship, it’s important to note that cu concentrations in sediment did not change much until ~2001, when the beginning of an extended drought period. Thus, the temporal trend is really driven by the last four years and may not be indicative a response to remediation.
The biomonitor shows a different pattern than sediment, with the highest concentrations in the middle of the time series (between 1996-1998). Again, this corresponds to periods of high flow (mid-1990’s).
This reach of the river is unique in that Cu concentrations in both indicators are influenced by annual hydrologic conditions unlike Reach A which shows no relationship to discharge.

## Slide 14
Flow conditions can also greatly influence the spatial gradient of metal…
Kilometers Downstream
Cu in Hydropsyche, µg/g
0
40
80
120
160
200
0
60
120
180
1993
1997
Notes: We’ve seen that flow conditions can greatly impact the temporal pattern of metal within a station (or reach), but hydrology can also impact the spatial gradient.
Here we see an example of a typical pre-remediation spatial gradient of metal distributed throughout the river (galen gage to turah). Note that the highest observed concentrations occur in the most upstream reach, a site closest to the source of metal. Metal concentrations decrease along a longitudinal gradient.
Next we compare this to a pattern observed during a high flow year (1997). Notice that the distribution of metals has changed to where the highest concentrations were found in the middle and lower reaches. Concentrations are lowest at the most upstream site, probably an influence of remediation.
So we’ve seen that hydrology can impact sites temporally (Reach B and C) but also spatially. As remediation progresses, it will be interesting to see if the pattern changes over time.

## Slide 15
Both indicators show a decline in Cu concentrations which corresponds to the timing of remediation.
This response is spatially restricted and can be seen only in the most upstream stations.
Some stations within the remediated reach (A) continue to be temporally variable and suggest areas of localized influences which supercede remediation to date.
Summary: Reach A
Notes: Summary related to upstream reach:
Note to first bullet: This is also true of dissolved Cu trends, an indicator not discussed here. Not necessarily true of all elements though (consider As pattern).
Note the third bullet: Can’t assume that all stations will respond similarly. There are areas of the river that are highly variable (perhaps due to localized inputs or process which ‘disconnect’ the upstream contaminant signature from impacting these sites.

## Slide 16
Hydrology continues to be an important influence in controlling the temporal and spatial pattern of metals in Reaches B and C.
Current monitoring has captured a range of hydrologic conditions that may provide insight into future trends as remediation progresses.
Ongoing monitoring is needed to determine if the relationship with hydrology changes as metal loadings are reduced.
Summary: Reach B & C
Notes: Summary related to downstream reach (B and C)
Note to first bullet: Thus, no evidence of remediation (at least not yet. Perhaps that will change as remediation moves into full scale operation).
Note to third bullet: Need to account for the unpredictable. We’ve already seen that unexpected patterns can emerge (Arsenic trend at PO, spatial gradient shift during high flow events). Especially important to track as remediation progresses.

## Slide 17
Luoma Project, USGS CA
Dan Cain
Cindy Brown
Robin Bouse
Robin Stewart
David Buchwalter
Jim Carter
Marie-Noële Croteau
Stacey Andrews
Ed Moon
Ellen Axtmann
Liz Duffy
CP David
Irene Lavigne
Chris Wellise
Kara Kemmler
USGS Helena MT
John Lambing
Kent Dodge
US EPA
Funding
USGS National Research Program
Acknowledgements