## Slide 1: Clark Fork River Metals TMDL Development
Eric Sivers
Senior TMDL Planner
esivers@mt.gov

## Slide 2: Outline
Relevant criteria and assessment
Current conditons
TMDL process overview
Source assessment
The outlook

## Slide 3
Recent Assessment
Metals impairments were assessed for the 2014 Integrated Report’s 303(d) list.
These TMDLs are based on the 2014 303(d) list.

## Slide 4: Water Quality Impairments
One or more uses is not supported
Uses depend on classification (B1, C1, etc.)
Relevant criteria depend on use
Notes: Classifications established in rule: ARM 17.30.606

## Slide 5: Waterbody Classifications

## Slide 6: Metals Numeric Water Quality Criteria
Chronic aquatic life criteria
Acute aquatic life criteria
Human health standard
LOWEST applicable of these is chosen as the target for TMDLs
Notes: Hardness dependent metals: cadmium, chromium, copper, lead, nickel, silver, zinc
Zn: hardness dependent, but chronic/acute levels are the same. Ag: acute only; no chronic
Some HHS far lower than ALC (As, Sb); some much higher (Cu, Zn)

## Slide 7: Hardness Dependent Criteria
For example, copper:
Higher hardness, higher allowable concentration of copper
Chronic aquatic life criteria at 100 mg/L hardness is 9.33 µg/L
Chronic aquatic life criteria at 50 mg/L hardness is 5.16 µg/L
HHS is fixed: 1,300 µg/L
Notes: Cu: chronic at 50mgL and 100mgL hardness = 5.16 µg/L and 9.33 µg/L ; acute = 7.29 µg/L and 14.0 µg/L
HHS is fixed at 1,300 µg/L

## Slide 8: Importance of Seasonality

## Slide 9
Metals Impairments
Notes: This project is a subset of the streams in the Clark Fork – Drummond and Middle Clark Fork Tributaries TPAs. Basically it’s all the metals-impaired streams in these planning areas.

## Slide 10: 2012 Arsenic Concentrations
High Flow
Low Flow

## Slide 11: 2012 Copper Concentrations
High Flow
Low Flow

## Slide 12: Metals vs. Targets

## Slide 13: Metals vs. Targets

## Slide 14: Metals vs. Targets

## Slide 15
What is a TMDL?
The amount of a pollutant a stream can
accept and still meet standards.
Think of it as a safe loading rate:
Notes: How much Yellow #5 and sugar can you consume safely? If there’s a set amount, that’s a numeric standard. If instead it’s: “stop before you turn yellow and slip into a diabetic coma”, that’s a narrative standard.

## Slide 16: Calculating the TMDL
A metals TMDL is an equation
TMDLs vary with flow: more water, greater allowable load.
TMDL = target x flow
(x conversion factor)

## Slide 17
Hardness-Dependent Metals
Notes: Hardness dependent metals: cadmium, chromium, copper, lead, nickel, silver, zinc
Zn: hardness dependent, but chronic/acute levels are the same. Ag: acute only; no chronic

## Slide 18
Hardness-Independent Metals
Increasing Streamflow →
Increasing Load →
Notes: Not shown: aluminum, selenium, antimony

## Slide 19
TMDL Model

## Slide 20: Allocations
TMDL is the pie; allocations are the pieces of the pie
TMDL = Σ WLAs + Σ LAs
Notes: AND a margin of safety.

## Slide 21: Two Kinds of Allocations:
TMDL = Sum of all allocations
Load allocations: nonpoint sources –tributaries, background & other diffuse sources
Wasteload allocations: point sources: permitted discharges, Superfund

## Slide 22: Point Sources

## Slide 23: WWTP WLA Approaches
Continue Existing Operation
End-of-Pipe
Staged

## Slide 24: ‘End-of-Pipe’ WLAs:
Target concentration at discharge
No assimilative capacity due to upstream impairment
Discharging at target concentration does not cause or contribute to impaired conditions
Allows addition of new discharges to a balanced TMDL equation

## Slide 25: Staged WLAs:
Usually based on end-of-pipe WLA
Infrastructure improvements
Provide schedule
Case-by-case for each permit

## Slide 26: ‘Continue Existing’ WLAs:
Discharge concentration may exceed target
Volume of discharge is low
Load contribution of <0.1%
Instream effect not measurable
Notes: In this document, these situations are associated with anticipated assimilative capacity.

## Slide 27: Superfund Mainstem OU WLAs:
Copper: Target x (Δ flow) – (WLA Deer Lodge)
Flow-based allowable increase in load over length of the segment
Minus any WLAs or LAs added over the segment

## Slide 28
Metals-Impaired Tributaries
Arsenic
Lead
Mercury
Arsenic
Lead
Arsenic
Notes: German Gulch Arsenic
Mill-Willow Bypass Arsenic, cadmium, copper, lead, zinc
Warm Springs Creek Arsenic, cadmium, copper, iron, lead, zinc
Lost Creek Arsenic, copper, lead
Modesty Creek Arsenic, cadmium, copper, lead
Peterson Creek Iron
Little Blackfoot River Arsenic, lead
Gold Creek Lead, iron
Dunkleberg Creek Arsenic, cadmium, copper, iron, lead, zinc
Flint Creek Arsenic, copper, iron, lead
Cramer Creek Lead
Wallace Creek Copper
Bitterroot River Copper, lead
Flat Creek Arsenic, cadmium, lead, zinc

## Slide 29: Clark Fork River
For each segment above the Blackfoot River:
TMDL = WLA NPL + ΣWLA WWTPs + ΣLA Tribs+ LA Upstream

## Slide 30: Clark Fork River
For each segment below the Blackfoot River:
TMDL = ΣWLA WWTPs + LA Trib + LA Upstream + LA Background
Notes: This LA tributary term is for the 1 metals-impaired tributary to each of these AUs. Unimpaired tributary contributions are included in the LA background.

## Slide 31: Predicting Assimilative Capacity:
Calculate metals load above TMDL
Compare downstream
e.g. lead: 161 lbs/day above Blackfoot, 80 lbs/day below

## Slide 32
Assimilative Capacity
Load
Load
Load
Downstream
TMDL
Excess Load

## Slide 33
Load
Load
Load
Downstream
Load Reduction
TMDL
Assimilative Capacity
Assimilative Capacity

## Slide 34: Assimilative Capacity Projections

## Slide 35
QUESTIONS?

## Slide 36: Clark Fork River Metals TMDL Development
Eric Sivers
Senior TMDL Planner
esivers@mt.gov